Radio Wave and Antenna Basics
Prepared by Joe Blankenship
Cyber Geography Research Institute International

---
Agenda
Radio Wave Propagation
Antenna Basics
Common Antennas
Safety & Resources
https://github.com/joeblankenship1

---
Radio Wave Propagation
- Electromagnetic Waves
  - Electricity (blue)
  - Magnetism (red)
  - A change in these creates waves
    - Electric field is perpendicular to the magnetic field
- No medium required
  - However, most of this course looks at EMR propagation through the atmosphere
    - EMR (electromagnetic radiation)
  - Particle and wave properties
    - Electron Volts
    - Hertz
[Speaker Notes: The most efficient antennas are built to the known wavelength of the frequency being used/interrogated. Example: 1 MHz = 984 ft.]

---
Radio Wave Propagation
- Speeds
  - 186,000 miles/second or 3 x 108 meters/second in a vacuum
  - Actual speeds are slightly slower due to impedance
- Wavelength is λ = V/F
  - λ = Wavelength in meters
  - V = Velocity (Speed of Radio Waves in meters per second)
  - F = Frequency in Hertz (HZ)
[Speaker Notes: The most efficient antennas are built to the known wavelength of the frequency being used/interrogated. Example: 1 MHz = 984 ft.]

---
Radio Wave Propagation
Band	Frequency
Very Low Freq. (VLF)	Below .03 (30 kHz)
Low Frequencies (LF)	.03 to .3 (30 to 300kHz)
Medium Freq. (MF)	.3 to 3.0 (300 kHz to 3 MHz)
High Freq. (HF)	3.0 to 30 MHz
Very High Freq. (VHF)	30 to 300 MHz
Ultrahigh Freq. (UHF)	300 to 3,000 MHz
Super High Freq. (SHF)	3,000 to 30,000 MHz / (3 to 30 GHz)
Extremely High Freq. (EHF)	30,000 to 300,000 MHz / (30 to 300 GHz)

---
Radio Wave Propagation
- Ground Waves travel along the surface of the earth
- Sky Waves travel from the transmitter to one of the ionospheric layers and is returned to the earth
  - Requires very little power to travel long distances, say around 8000 miles (~12874 Km)
- Atmosphere is subject to seasonal changes that affect signals
  - The troposphere, stratosphere, ionosphere
[Speaker Notes: There are Four Layers in the Ionosphere. During the Day, all Four Layers are present. At Night, the F1 and F2 layers thin out and tend to merge into one layer. The D and E layers disappear.]

---
Radio Wave Propagation
[Speaker Notes: variables in a sky wave signal—the frequency, the ionospheric layers, the time of day, the season, and the sunspot cycle variables in a ground wave signal depend on the terrain over which it travels]

---
Radio Wave Propagation
- Reflection (at same angle it strikes)
  - Metal surfaces, water
- Refraction (bending of signal through object)
- Diffraction (bending of signal around object)
  - Creates shadow zones
- Absorption (agitation of object's matter; heat generated)
- Scatter (multi-directional bounce of signal from object)
- Man-made and natural objects
  - Foliage, power lines, buildings, bridges
- Critical Frequency
  - Frequencies higher than the critical frequency will pass through the layer sans refraction
  - As a radio wave passes through a layer, it is partially absorbed

---
Radio Wave Propagation
- Minimum Power for transmission
  - Depends on minimum power required by reciever(s)
http://transition.fcc.gov/pshs/techtopics/techtopics17.html

---
Radio Wave Propagation
Band	Ground Wave	Sky Wave	Power Required (kW)
LF	0 - 1,000 Miles / (0 - 1,609 km)	500 - 8,000 Miles / (835 - 12,872 km)	Above 50 kW
MF	0 – 100 Miles / (0 – 161 km)	100 – 1,500 Miles / (161 – 2,415 km)	.5 – 50 kW
HF	0 – 50 Miles / (0 – 83 km)	100 – 8,000 Miles / (161 – 12,872 km)	.5 – 5 kW
VHF	0 – 30 Miles / (0 – 48 km)	50 – 150 Miles / (83.5 – 241 km)	.5 or less kW
UHF	0 – 50 Miles / (0 – 83 km)	N/A	.5 or less kW

---
Radio Wave Propagation
- Sunspots
  - In cycles, vary yearly, distances of 500,000+ miles
  - High activity, high frequency; Low, low
  - Generally, higher freq. during the day, low at night
- Other signals
  - Overlapping frequencies
  - With low power, a way to mask other signals
  - With high power, a way to jam or repeat

---
Radio Wave Propagation
Break and/or Questions?

---
Antenna Basics
- In its simplest form...
  - It is a conductor that is designed to provide “the most attractive path” to ground for a signal
  - The antenna...
    - Uses a transmission line...
      - To transmit/receive/both your data via a carrier from a load
        - Grounded within a designed system

---
Antenna Basics
- Antenna Usage
  - Transmission
  - Reception
  - Proper design will permit sustained characteristics for transmission and reception
  - However...
    - Certain antennas have materials/components that will not allow for transmission as most are built for just reception
    - Exam specification carefully!

---
Antenna Basics
- Antenna Wavelength
  - Shape and size of an antenna is dependent on the wavelength and format of the signal
  - Peak to peak, trough to trough
  - Antenna length
    - Constant  Frequency in MHz = Antenna Length in Feet and Inches (or meters)
      - 234 (71.32) for a ¼ wavelength antenna
      - 468 (142.65) for a ½ wavelength antenna (Best for expedient use, but 5 full wavelengths provides the optimum antenna length for any given frequency)
      - 936 (285.29) for a full wavelength antenna
      - Antenna should be cut a little longer than calculated to ensure good SWR!
[Speaker Notes: ¼ Wavelength antenna at 12.000 MHz 234  12 = 19.5 Answer = The antenna length for a ¼ wave antenna at 12 MHz is 19 Feet 6 Inches long.]

---
Antenna Basics
- In general
  - Lower frequency, longer antenna; higher, shorter
  - Antennas are only good for a certain set of frequencies (frequency response)
    - Choose the best compromise between range and efficiency
    - Very task dependent
  - Examine Smith Chart if available
  - Standing Wave Ratio!!!

---
Antenna Basics
- Standing Wave Ratio!!!
  - Extremely Important
  - When properly cut, sine wave begins at one end of the antenna and ends at the other end of the antenna
  - When NOT, the sine wave doesn’t match the antenna length, causing standing waves or reflected waves
    - High SWR leads to no transmission and/or feedback
    - SWR between line and load should
      be less than 1.5 to 1;
      up to 3 to 1 will work... kinda

---
Antenna Basics
- Antenna polarization
  - Vertical
  - Horizontal
  - Circular
    - Both vertical and horizontal
  - Everywhere in between
    - Depends on the orientation of the emission vector for the wave in relationship to the earth
    - A wave transmitted by a vertical antenna
      - Will have a vertically polarized signal
        - Which will need to be received by
          - A vertically polarized antenna
  - Difference in polarization causes loss of signal!

---
Antenna Basics
- Antenna Directivity
  - How well an antenna transmits/receives in different direction(s)
  - Radiation patterns (Smith Charts AGAIN!)
    - Omni-directional
    - Directional
      - Beam of the antenna
        - Narrow
        - Wide
      - Take-off Angle
      - Side Lobes

---
Antenna Basics

---
Antenna Basics
- Antenna Gain
  - Directly related to directivity
  - Inverse Square Law
    - Signal strength for a given surface area is inversely proportional to the distance it traveled from the source
- Antenna Loss
  - Impedance everywhere
  - Both internal to the system
  - And external to the antenna

---
Antenna Basics
- Antenna Signal Strength
  - More power, more distance
  - HOWEVER...
    - A properly designed antenna will transmit to the proper distance with less power consumption
  - Different consideration based on design
    - Omnidirectional vs. Directional
    - Environmental Factors
    - Operational Considerations
    - And last but not least...

---
Antenna Basics
- Antenna Signal Strength
  - Legal Considerations!
    - The largest of party poopers
    - Ensure compliance with local, state, and federal laws
      - This also especially applies to international laws when abroad
- Antenna Noise
  - Internal Causes
    - Faulty connections, failing components, damages
  - External Causes
    - Power lines, other transmissions, motors
  - Mitigation through AGC, filters, design, location selection, etc.

---
Antenna Basics
- After looking at the aspects of the antenna itself, we move to what feeds the antenna
- Transmission Lines
  - Aka feeder lines
  - Resonant or tuned (same length as antenna)
  - Non-resonant or un-tuned (SWR < 1.5)
    - Impedance of antenna and line have to match
  - Length (in Meters) = (300/CF) * VF
    - VF = Velocity Factor (depends on type of cable)
    - CF = Center Frequency

---
Antenna Basics
- Transmission Lines
  - Types
    - Single Wire (earth return path)
      - Used as non-resonant feeder line
    - Twisted Pair (high loss; no use above 15 MHz)
      - Shielded or unshielded; not the best (worse when wet)
    - Ladder Line or Ribbon Line
      - Unshielded and constantly spaced
    - Coaxial (minimum loss; loss increase with frequency increase)
  - Power Loss
    - Radiation (line radiates like antenna)
    - Heating (current flow causes heat; eddy currents)
    - Reflection (traveling waves from transmitter)

---
Antenna Basics
- Antenna Insulation
  - The transmitting/receiving element of the antenna must be isolated from ground
  - Remember, you're trying to direct the signal through the antenna
    - Through the transmission line
      - Through the Radio
        - And THEN to ground
  - Should be designed for ahead of time
  - However, any nonconductor should work in a pinch

---
Antenna Basics
- Antenna Counterpoise
  - Prevent ground reflected waves from absorption
    - Artificial reflective surface such as...
      - A suspended wire above the ground
      - Series of suspended wires
      - Moistened earth or a puddle
    - 3-5 feet separation between the antenna and counterpoise
- Antenna Resistors
  - To make a bi-directional antenna unidirectional
    - Maximizes directional output

---
Antenna Basics
Bleeder resistor for static with counterpoise
Antenna resistors for directionality

---
Antenna Basics
Break and/or Questions?

---
Common Antennas
- Horizontal Antennas
  - Suggested max resistance is 100 ohms
  - Quarter wavelength above the ground
  - Practical Half-wave Antennas
    - The ground has the greatest effect on the Medium and High Frequency antennas that are mounted fairly close to it in terms of wavelength.
    - Transmit - some of the energy travels directly to the distant station, and part of the energy strikes the ground directly in front of the antenna and a 180º phase shift (Phase Reversal) takes place
      - This may cancel out the direct wave if they arrive at the same time and are out of phase—creating a Null effect.
      - If they arrive in phase, the ground reflected wave adds to the direct wave, making it stronger.

---
Common Antennas
- Horizontal Antennas
  - Dipole Antenna
    - 2-30 MHz
    - Coax feeder line
    - Feeder line at right angle to antenna
      - Reduce radiation
      - Reduce coupling feedback
    - Counterpoise can be used if there are perceived issues
  - Others
    - 14% off centered
    - Inverted L
    - Sloping wire (73 ohm impedance)
      - Best compromise for ground and sky wave utility!

---
Common Antennas
- Grounded Antennas
  - Quarter wave antennas
    - Used with highly conductive ground
    - A ground rod uses the earth as the other ¼ wavelength element (an image antenna)

---
Common Antennas
- Ground Plane Antennas
  - 1 section vertical ¼ wavelength
  - N number of spokes ¼ wavelength
    - Form an artificial ground
    - VHF or higher frequencies
  - Example
    - Disc-cone Antenna

---
Common Antennas
- ADS-B Antenna
  - http://revision3.com/hak5/how-to-build-an-ads-b-antenna/

---
Common Antenna
- Other
  - Fractal Antenna
    - Multilevel or space filling antennas
    - Popular for RFID
    - Uses a repeating iterations of a set shape to maximize the receptive capability of the antenna over a greater range
  - “Cantenna”
    - Directional wave guide antenna
    - Name says it all...
    - Common for WiFi applications

---
Common Antennas
- Usage
  - Calculations for the type of antenna, angle, distance, lines, etc. are based on your best knowledge of the signal strength, format, and location.
  - Your wavelength and design must match as close as possible to the known signal parameters
  - Don't get in trouble!
  - Do no harm!

---
Safety Concerns
- When dealing with electricity, deal with it appropriately (protective gear and posture as required)
- When erecting antennas, ensure proper gear is used when:
  - Climbing or descending from heights
  - Building masts or other structures to house antenna
  - Assessing environment specific concerns
  - Bad weather conditions
- Wear “protective glasses” just in case
- When in doubt, ground it!

---
Resources
- ARRL
  - http://www.arrl.org/
- DXZone
  - http://www.dxzone.com/
- AMSAT
  - http://www.amsat.org/
- Antenna design programs
  - Several available online (download and web-based)
- For all else...
  - Go forth and Google!

---
That's all folks!
Questions?
Prepared by Joe Blankenship
Cyber Geography Research Institute International